## Slide 1: DOT PRODUCT
  In-Class Activities:
  Check Homework
  Reading Quiz
  Applications / Relevance
  Dot product - Definition
  Angle Determination
  Determining the Projection
  Concept Quiz
  Group Problem Solving
  Attention Quiz
Today’s Objective:
Students will be able to use the vector dot product to:
a) determine an angle between two vectors and,
b) determine the projection of a vector along a specified line.

## Slide 2: READING QUIZ
1. The dot product of two vectors P and Q is defined as
A) P Q sin  B) P Q cos 
C) P Q tan  D) P Q sec 
2. The dot product of two vectors results in a _________ quantity.
A) Scalar B) Vector
C) Complex D) Zero
P
Q

Notes: Answers:
1. B
2. A

## Slide 3: APPLICATIONS
If you know the physical locations of the four cable ends, how could you calculate the angle between the cables at the common anchor?

## Slide 4: APPLICATIONS (continued)
For the force F applied to the wrench at Point A, what component of it actually helps turn the bolt (i.e., the force component acting perpendicular to arm AB of the pipe)?

## Slide 5: DEFINITION
The dot product of vectors A and B is defined as A•B = A B cos .
The angle  is the smallest angle between the two vectors and is always in a range of 0º to 180º.
Dot Product Characteristics:
1. The result of the dot product is a scalar (a positive or negative number).
2. The units of the dot product will be the product of the units of the A and B vectors.

## Slide 6: DOT PRODUCT DEFINITON (continued)
Examples: By definition, i • j = 0
i • i = 1
A • B = (Ax i + Ay j + Az k) • (Bx i + By j + Bz k)
= Ax Bx + AyBy + AzBz

## Slide 7: USING THE DOT PRODUCT TO DETERMINE THE ANGLE BETWEEN TWO VECTORS
For these two vectors in Cartesian form, one can find the angle by
a) Find the dot product, A • B = (AxBx + AyBy + AzBz ),
b) Find the magnitudes (A & B) of the vectors A & B, and
c) Use the definition of dot product and solve for , i.e.,
 = cos-1 [(A • B)/(A B)], where 0º    180º .

## Slide 8: DETERMINING THE PROJECTION OF A VECTOR
Steps:
1. Find the unit vector, ua along line aa
2. Find the scalar projection of A along line aa by
A|| = A • ua = Ax ux + Ay uy + Az uz
You can determine the components of a vector parallel and perpendicular to a line using the dot product.

## Slide 9: DETERMINING THE PROJECTION OF A VECTOR (continued)
3. If needed, the projection can be written as a vector, A|| , by using the unit vector ua and the magnitude found in step 2.
A|| = A|| ua
4. The scalar and vector forms of the perpendicular component can easily be obtained by
A  = (A 2 - A|| 2) ½ and
A  = A – A||
(rearranging the vector sum of A = A + A|| )

## Slide 10: EXAMPLE I
Plan:
1. Find rAO
2. Find the angle  = cos-1{(F • rAO)/(F rAO)}
3. Find the projection via FAO = F • uAO (or F cos  )
Given: The force acting on the hook at point A.
Find: The angle between the force vector and the line AO, and the magnitude of the projection of the force along the line AO.
Notes: Source : F2-25

## Slide 11: EXAMPLE I (continued)
rAO = {1 i + 2 j  2 k} m
rAO = {(-1)2 + 22 + (-2)2}1/2 = 3 m
F = { 6 i + 9 j + 3 k} kN
F = {(-6)2 + 92 + 32}1/2 = 11.22 kN
 = cos-1{(F • rAO)/(F rAO)}
 = cos-1 {18 / (11.22  3)} = 57.67°
F • rAO = ( 6)(1) + (9)(2) + (3)(2) = 18 kNm

## Slide 12: EXAMPLE I(continued)
uAO = rAO / rAO = (1/3) i + (2/3) j + (2/3) k
FAO = F • uAO = ( 6)(1/3) + (9)(2/3) + (3)(2/3) = 6.00 kN
Or: FAO = F cos  = 11.22 cos (57.67°) = 6.00 kN

## Slide 13: EXAMPLE II
Plan:
1. Find F, rOA and uOA
2. Determine the parallel component of F using F|| = F • uOA
3. The perpendicular component of F is F = (F2 - F|| 2) ½
Given: The force acting on the pole at point A.
Find: The components of the force acting parallel and perpendicular to the axis of the pole.
Notes: Source : F2-30

## Slide 14: EXAMPLE II (continued)
rOA = {4 i + 4 j + 2 k} m
rOA = {(-4)2 + 42 + 22}1/2 = 6 m
uOA = 2/3 i + 2/3 j + 1/3 k
F = {-(600 cos 60°) sin30° i + (600 cos 60°) cos30° j + (600 sin 60°) k} lb
F = {-150 i + 259.8 j + 519.6 k} lb
The parallel component of F :
F|| = F • uOA ={-150 i + 259.8 j + 519.6 k}• {-2/3 i + 2/3 j + 1/3 k}
F|| = (-150) × (-2/3) + 259.8 × (2/3) + 519.6 × (1/3) = 446 lb

## Slide 15: EXAMPLE II (continued)
The perpendicular component of F :
F = (F2 - F|| 2) ½ = ( 600 2 – 446 2) ½ = 401 lb
F = 600 lb
F|| = 446 lb

## Slide 16: CONCEPT QUIZ
1. If a dot product of two non-zero vectors is 0, then the two vectors must be _____________ to each other.
A) Parallel (pointing in the same direction)
B) Parallel (pointing in the opposite direction)
C) Perpendicular
D) Cannot be determined.
2. If a dot product of two non-zero vectors equals -1, then the vectors must be ________ to each other.
A) Collinear but pointing in the opposite direction
B) Parallel (pointing in the opposite direction)
C) Perpendicular
D) Cannot be determined.
Notes: Answers:
1. C
2. A

## Slide 17: GROUP PROBLEM SOLVING
Plan:
1. Find rOA and uOA
2. Find the angle  = cos-1{(F • rOA)/(F × rOA)}
3. Then find the projection via FOA = F • uOA or F (1) cos 
Given: The 300 N force acting on the bracket.
Find: The magnitude of the projected component of this force acting along line OA
Notes: Source : P2-137

## Slide 18: GROUP PROBLEM SOLVING (continued)
rOA = {0.450 i + 0.300 j + 0.260 k} m
rOA = {(0.450)2 + 0.3002 + 0.2602 }1/2 = 0.60 m
uOA = rOA / rOA = {-0.75 i + 0.50 j + 0.433 k }
F´

## Slide 19: GROUP PROBLEM SOLVING (continued)
F = {150 sin 30°i + 300 cos 30°j + 150 cos 30°k} N
F = {75 i + 259.8 j + 129.9 k} N
F = {(-75)2 + 259.82 + 129.92}1/2 = 300 N
F´
F´ = 300 sin 30° = 150 N

## Slide 20: GROUP PROBLEM SOLVING (continued)
 = cos-1{(F • rOA)/(F × rOA)}
 = cos-1{145.5 /(300 × 0.60)} = 36.1°
Or
FOA = F cos  = 300 cos 36.1° = 242 N
F • rOA = (-75) (-0.45) + (259.8) (0.30) + (129.9) (0.26)
= 145.5 N·m
FOA = F • uOA = (-75)(-0.75) + (259.8) (0.50) + (129.9) (0.433) = 242 N
The magnitude of the projected component of F along line OA will be

## Slide 21: ATTENTION QUIZ
1. The dot product can be used to find all of the following except ____ .
A) sum of two vectors
B) angle between two vectors
C) component of a vector parallel to another line
D) component of a vector perpendicular to another line
2. Find the dot product of the two vectors P and Q.
P = {5 i + 2 j + 3 k} m
Q = {-2 i + 5 j + 4 k} m
A) -12 m B) 12 m C) 12 m 2
D) -12 m 2 E) 10 m 2
Notes: Answers:
1. A
2. C

## Slide 22
End of the Lecture
Let Learning Continue